## Slide 1
Unit 14
This chapter in the book includes:
Objectives
Study Guide
14.1 Design of a Sequence Detector
14.2 More Complex Design Problems
14.3 Guidelines for Construction of State Graphs
14.4 Serial Data Code Conversion
14.5 Alphanumeric State Graph Notation
Programmed Exercises
Problems
Derivation of State Graphs and Tables

## Slide 2: Objectives
Given a problem statement for the design of a Mealy or Moore
sequential circuit, find the corresponding state graph and table.
2. Explain the significance of each state in your graph or table
in terms of the input sequences required to reach that state.
3. Check your state graph using appropriate input sequences.

## Slide 3: 14.1 Design of a Sequence Detector
Fig 14-1 Sequence Detector (finding ‘101’) to be Designed
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)
Search engine
Chat GPT
Notes: avian influenza virus

## Slide 4: 14.1 Design of a Sequence Detector
Fig 14-2 & 14-3 Formation of State Graph (finding ‘101’) (Mealy)
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)
Peace
Stand by
Alarm
Fire

## Slide 5: 14.1 Design of a Sequence Detector
Fig 14-4 Mealy State Graph for Sequence Detector (finding ‘101’)
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)

## Slide 6: 14.1 Design of a Sequence Detector
Table 14-1 State Table
Present state |  | Next State |  | Present Output | 
 |  | X = 0 | X = 1 | X = 0 | X =1
S0 S1 S2 |  | S0 S2 S0 | S1 S1 S1 | 0 0 0 | 0 0 1
AB |  | A+ B+ |  | Z | 
 |  | X = 0 | X = 1 | X = 0 | X =1
00 01 10 |  | 00 10 00 | 01 01 01 | 0 0 0 | 0 0 1
Table 14-2 Transition Table with State Assignment

## Slide 7: 14.1 Design of a Sequence Detector
Maps for the next states A+ and B+ and the output function Z

## Slide 8: 14.1 Design of a Sequence Detector
Fig 14-5 Final Circuit

## Slide 9: 14.1 Design of a Sequence Detector
Moore Machine Design Process
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)
Peace
Stand by
Alarm
Fire

## Slide 10: 14.1 Design of a Sequence Detector
Fig 14-6 Moore State Graph for Sequence Detector
X = | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0
Z = | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
(time: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15)
Each state includes output.
That’s why Moore type has one more state (S3)

## Slide 11: 14.1 Design of a Sequence Detector
Table 14-3 State Table
Present state |  | Next State |  | Present Output (Z)
 |  | X = 0 | X = 1 | 
S0 S1 S2 S3 |  | S0 S2 S0 S2 | S1 S1 S3 S1 | 0 0 0 1
AB |  | A+ B+ |  | Z
 |  | X = 0 | X = 1 | 
00 01 11 10 |  | 00 11 00 11 | 01 01 10 01 | 0 0 0 1
Table 14-4 Transition Table with State assignment
10
11
11
01

## Slide 12: 14.2 More Complex Design Problems
X= | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
 |  |  |  | ↑ |  | ↑ |  | ↑ | ↑ |  |  |  | ↑ |  | ↑ |  | 
 |  |  |  | a |  | b |  | c | d |  |  |  | e |  | f |  | 
Z= | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
The circuit to be designed (Mealy):
Output Z=1 if input sequence ends in either 010 or 1001

## Slide 13: 14.2 More Complex Design Problems
Fig 14-8 Formation of state graph (step1)
reset
0
01
010
S0
S1
S2
S3
sequence received
state
010 or 1001
X= | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
 |  |  |  | ↑ |  | ↑ |  | ↑ | ↑ |  |  |  | ↑ |  | ↑ |  | 
 |  |  |  | a |  | b |  | c | d |  |  |  | e |  | f |  | 
Z= | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
No inputs

## Slide 14: 14.2 More Complex Design Problems
Fig 14-9 Formation of state graph (step2)
reset
0 (but not 10)
01
10
1 (but not 01)
100
S0
S1
S2
S3
S4
S5
sequence ends in
state
010 or 1001

## Slide 15: 14.2 More Complex Design Problems
Fig 14-10 Completed State Graph for a Sequence Detector to be Designed
reset
0 (but not 10)
01
10
1 (but not 01)
100
S0
S1
S2
S3
S4
S5
sequence ends in
state
010 or 1001

## Slide 16: 14.2 More Complex Design Problems
X = | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
 | ↑ |  |  | ↑ |  | ↑ | ↑ | ↑
 | a |  |  | b |  | c | d | e
Z = | (0) | 0 | 0 | 0 | 0 | 1 | 0 | 1
The circuit to be designed (Moore)
Output Z=1 if the total number of 1’s received is odd and at least two consecutive 0’s have been received

## Slide 17: 14.2 More Complex Design Problems
Fig 14-11 Formation of state graph (step1)

## Slide 18: 14.2 More Complex Design Problems
Fig 14-12 Formation of state graph (step2)
state | sequence ends in
S0 S1 S2 S3 S4 | reset or even 1’s odd 1’s even 1’s and ends in 0 even 1’s and 00 has occurred 00 has occurred and odd 1’s

## Slide 19: 14.2 More Complex Design Problems
Fig 14-13 Completed State Graph for a Sequence Detector to be Designed
state | sequence ends in
S0 S1 S2 S3 S4 S5 | reset or even 1’s odd 1’s even 1’s and ends in 0 even 1’s and 00 has occurred odd 1’s and 00 has occurred odd 1’s and ends in 0

## Slide 20
14.3 Guidelines for Construction of State Graphs
1. Construct some sample input and output sequences to make sure that you understand the problem statement.
2. Determine under what conditions the circuit should reset to its initial state.
3. If only one or two sequences lead to a non-zero output, a good way to start is to construct a partial state graph for those sequences.
4. Determine what sequences or groups of sequences must be remembered by the circuit and set up states accordingly.
5. Each time you add an arrow to the state graph, determine it can go to one of the previously defined states or whether a new state must be added.
6. Check your state graph to make sure there is one and only one path leaving each state for each combination of values of the input variables.
7. When your state graph is complete, test it by applying the input sequences formulated in part 1 and making sure the output sequences are correct.

## Slide 21: 14.3 Guidelines for Construction of State Graphs
Example 1: Z=1 when input sequence 0101 or 1001 occurs.
The circuit resets after every four inputs. (Mealy Circuit)
X = | 0101 | 0010 | 1001 | 0100
Z = | 0001 | 0000 | 0001 | 0000
A typical sequence of input and output

## Slide 22: 14.3 Guidelines for Construction of State Graphs
Fig 14-14 Partial State Graph for Example 1
state | sequence received
S0 S1 S2 S3 S4 | Reset 0 1 01 or 10 010 or 100
Targets : 0101 or 1001
Target 1 : 0101

## Slide 23: 14.3 Guidelines for Construction of State Graphs
Fig 14-14 Partial State Graph for Example 1
state | sequence received
S0 S1 S2 S3 S4 | Reset 0 1 01 or 10 010 or 100
Target 2 : 1001

## Slide 24: 14.3 Guidelines for Construction of State Graphs
Fig 14-15 Complete State Graph for Example 1
state | sequence received
S0 S1 S2 S3 S4 S5 S6 | Reset 0 1 01 or 10 010 or 100 two inputs received, no 1 output is possible three inputs received, no 1 output is possible
0101 or 1001

## Slide 25: 14.3 Guidelines for Construction of State Graphs
Example 2: Z1=1 every time the input sequence 100 is completed
Z2=1 every time the input sequence 010 is completed
Once Z2=1 occurred, Z1=1 can never occur but not vice versa
Mealy circuit
X | = | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
Z1 | = | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Z2 | = | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
A typical sequence of input and output

## Slide 26: 14.3 Guidelines for Construction of State Graphs
Fig 14-16 Partial Graphs for Example 2
100 or 010 Mealy

## Slide 27: 14.3 Guidelines for Construction of State Graphs
Fig 14-17 State Graphs for Example 2
100 or 010 Mealy

## Slide 28: 14.3 Guidelines for Construction of State Graphs
Table 14-5 State Descriptions for Example 2
stats | Description |  | 
S0 S1 S2 S3 S4 | No progress on 100 Progress of 1 on 100 Progress of 10 on 100 No progress on 100 Progress of 10 on 100 | No progress on 010 No progress on 010 Progress of 0 on 010 Progress of 0 on 010 Progress of 01 on 010 | 010 has never occurred
S5 S6 S7 |  | Progress of 0 on 010 Progress of 01 on 010 No progress on 010 | 010 has occurred

## Slide 29: 14.3 Guidelines for Construction of State Graphs
Table 14-6
Present state |  | Next X = 0 | State X = 1 |  | Output X = 0 | (Z1 Z2) X = 1
S0 S1 S2 S3 S4 S5 S6 S7 |  | S3 S2 S3 S3 S5 S5 S5 S5 | S1 S1 S4 S4 S1 S6 S7 S7 |  | 00 00 10 00 01 00 01 00 | 00 00 00 00 00 00 00 00

## Slide 30: 14.3 Guidelines for Construction of State Graphs
Example 3: Two inputs – X1, X2, One output – Z
(a) The input sequence X1X2=01, 11 cause the output 0
(b) The input sequence X1X2=10, 11 cause the output 1
(c) The input sequence X1X2=10, 01 cause the output to change
Derive a Moore state graph
Previous Input (X1X2) | Output (Z) | State Designation
00 or 11 00 or 11 01 01 10 10 | 0 1 0 1 0 1 | S0 S1 S2 S3 S4 S5
SKIPPED

## Slide 31: 14.3 Guidelines for Construction of State Graphs
Table 14-7 State table
Present |  | Z |  |  | Next state |  |  | 
State |  |  | X1X2 | = | 00 | 01 | 11 | 10
S0 S1 S2 S3 S4 S5 |  | 0 1 0 1 0 1 |  |  | S0 S1 S0 S1 S0 S1 | S2 S3 S2 S3 S3 S2 | S0 S1 S0 S0 S1 S1 | S4 S5 S4 S5 S4 S5

## Slide 32: 14.3 Guidelines for Construction of State Graphs
Fig 14-18 State Graph

## Slide 33: 14.4 Serial Data Code Conversion
Fig 14-19 Serial Data Transmission

## Slide 34: 14.4 Serial Data Code Conversion
Fig 14-20 Coding Schemes for Serial Data Transmission
RZ : Return to Zero
NRZ: Non Return to Zero
NRZI: Non Return to Zero Inverted
Manchester: start with low for 0, with high for 1

## Slide 35: 14.4 Serial Data Code Conversion
Clock2 = clock * 2
glitch, hazard
Actual transmitted bit-stream
0 1 1 1 0 0 1 0
Fig 14-21 Mealy circuit for NRZ-to-Manchester Conversion
Clock2 = Clock*2

## Slide 36: 14.4 Serial Data Code Conversion
0
1
-
X = 0
Output (Z)
1
-
0
X = 1
S2
-
S0
X = 1
S1
S0
-
X = 0
Next State
S0
S1
S2
State
Present
(d) State table
Fig 14-21 Mealy circuit for NRZ-to-Manchester Conversion
The only possible input sequences : “00” and “11”.
0
1

## Slide 37: 14.4 Serial Data Code Conversion
Fig 14-22 Moore Circuit for NRZ-to-Manchester Conversion
Falling edge
0 1 1 1 0 0 1 0
0 1 1 1 0 0 1 0
Actual transmitted bit-stream
1 clock delay, but no glitch

## Slide 38: 14.4 Serial Data Code Conversion
Fig 14-22 Moore Circuit for NRZ-to-Manchester Conversion
0
0
1
1
Output (Z)
Present
S3
-
S3
S0
X = 1
S1
S2
S1
-
X = 0
Next State
S0
S1
S2
S3
State
Present
(c) State table
No inputs
Single zero
Double zero
Single one

## Slide 39: 14.5 Alphanumeric State Graph Notation
Fig 14-23 State Graphs with Variable Names on Arc Labels
F: forward
R: reverse
F=R=0 (?)
F=R=1 (?)
F has higher priority

## Slide 40: 14.5 Alphanumeric State Graph Notation
Table 14-8 State Table for Fig 14-23
PS | NS |  |  |  |  | Output |  | 
 | FR = | 00 | 01 | 10 | 11 | Z1 | Z2 | Z3
S0 S1 S2 |  | S0 S1 S2 | S2 S0 S1 | S1 S2 S0 | S1 S2 S0 | 1 0 0 | 0 1 0 | 0 0 1
If we AND together every possible pair of arc labels emanating from S0, we get
If we OR together all of the arc labels for state S0, we get

## Slide 41: 14.6 Incompletely Specified State Tables
A Mealy model sequential circuit examines the input sequence and generates an output of 1 when the last bit of a BCD digit is received if the parity of the digit is even;
Otherwise, the sequential circuit output is 0.
BCD Parity Detector

## Slide 42: 14.6 Incompletely Specified State Tables
BCD Parity Detector

## Slide 43: 14.6 Incompletely Specified State Tables
SG for BCD Parity Detector (Steve’s way)
S
S0
S1
S
S3
S
S2
S
S4
S
S5
S
S6
S
S7
S
0/0
1/0
0/0
0/0
1/0
0/0
1/0
1/0
0/0
1/?
1/?
0/1
1/0
0/0
1/1
state | Received & even/odd
S0 S1 S2 S3 S4 S5 S6 S7 | Reset 0 even 1 odd 00 even 01 odd 10 odd 011 even 001/100/010 odd
1/? -> out of BCD range -> Don’t cares

## Slide 44: 14.6 Incompletely Specified State Tables
101 Detector (Refer Section 15.5)