## Slide 1
Unit 4
This chapter in the book includes:
Objectives
Study Guide
4.1 Conversion of English Sentences to Boolean equations
4.2 Combinational Logic Design Using a Truth Table
4.3 Minterm and Maxterm Expansions
4.4 General Minterm and Maxterm Expansions
4.5 Incompletely Specified Functions
4.6 Examples of Truth Table Construction
4.7 Design of Binary Adders and Subtracters
Applications of Boolean Algebra/ Minterm and Maxterm Expansions

## Slide 2
Conversion of English Sentences to Boolean Equations
Combinational Logic Design Using a Truth Table
Minterm and Maxterm Expansions
General Minterm and Maxterm Expansions
Incompletely Specified Functions (Don’t care term)
Examples of Truth Table Construction
Design of Binary Adders(Full adder) and Subtracters
Objectives

## Slide 3: 4.1 Conversion of English Sentences to Boolean Equations
Find switching function which specifies the desired behavior of the circuit
Find a simplified algebraic expression for the function
Realize the simplified function using available logic elements
- Steps in designing a single-output combinational switching circuit
1. F is ‘true’ if A and B are both ‘true’  F = AB

## Slide 4
4.1 Conversion of English Sentences to Boolean Equations
1. The alarm will ring (Z) iff the alarm switch is turned on (A) and the door is not closed (B’), or it is after 6 PM (C) and window is not closed (D’)
2. Boolean Equation
3. Circuit realization

## Slide 5
Combinational Circuit with Truth Table
Using the expression for f=1 
4.2 Combinational Logic Design Using a Truth Table

## Slide 6
Simplified equation 
Circuit realization 
Original equation 
4.2 Combinational Logic Design Using a Truth Table

## Slide 7
Combinational Circuit with Truth Table
Using the expression for f=0 
When expression for f ’=1 
and take the complement of f ‘
4.2 Combinational Logic Design Using a Truth Table

## Slide 8: 4.3 Minterm and Maxterm Expansions
literal is a variable or its complement (e.g. A, A’)
Minterm, Maxterm for three variables

## Slide 9
Minterm of n variables is a product of n literals in which each variable appears exactly once in either true (A) or complemented form(A’), but not both. ( m0)
Minterm expansion
Standard Sum of Product 
4.3 Minterm and Maxterm Expansions

## Slide 10
Maxterm of n variables is a sum of n literals in which each variable appears exactly once in either true (A) or complemented form(A’) , but not both.( M0)
Maxterm expansion
Standard Product of Sum 
4.3 Minterm and Maxterm Expansions

## Slide 11
4.3 Minterm and Maxterm Expansions
Minterm and Maxterm expansions are complement each other

## Slide 12: 4.4 General Minterm and Maxterm Expansions
General truth table for 3 variables
ai is either ‘0’ or ‘1’
Maxterm expansion for general function
ai =1, minterm mi is present
ai =0, minterm mi is not present
ai =1, ai + Mi =1 , Maxterm Mi is not present
ai =0, Maxterm is present
Minterm expansion for general function

## Slide 13
 All minterm which are not present in F are present in F ‘
 All maxterm which are not present in F are present in F ‘
4.4 General Minterm and Maxterm Expansions

## Slide 14: 4.4 General Minterm and Maxterm Expansions
If i and j are different, mi mj = 0
Example
å
=
=
)
14
,
13
,
11
,
9
,
3
,
0
(
and
)
11
,
9
,
5
,
3
,
2
,
0
(
2
1
m
f
m
f
å

## Slide 15: Conversion between minterm and maxterm expansions of F and F’
 | Minterm Expansion of F | Maxterm Expansion of F | Minterm Expansion of F’ | Maxterm Expansion of F’
Minterm Expansion of F |  | Maxterm nos. are those nos. not on the minterm list for F | List minterms not present in F | Maxterm nos. are the same as minterm nos. of F
Maxterm Expansion of F | Minterm nos. are those nos. not on the maxterm list for F |  | Minterm nos. are the same as maxterm nos. of F | List maxterms not present in F
DESIRED FORM
GIVEN FORM

## Slide 16: Conversion between minterm and maxterm expansions of F and F’
Example

## Slide 17: 4.5 Incompletely Specified Functions
If N1 output does not generate all possible combination of A,B,C, the output of N2 (F) has ‘don’t care’ values.
Truth Table with Don’t Cares

## Slide 18: 4.5 Incompletely Specified Functions
Finding Function
Case 1: assign ‘0’ on X’s
Case 2: assign ‘1’ to the first X and ‘0’ to the second ‘X’
Case 3: assign ‘1’ on X’s
 The case 2 leads to the simplest function

## Slide 19
4.5 Incompletely Specified Functions
Minterm expansion for incompletely specified function
Don’t Cares
Maxterm expansion for incompletely specified function

## Slide 20: 4.6 Examples of Truth Table Construction
Example 1 : Half Adder
a b | Result | 
0 0 | 0 0 | 0+0=0
0 1 | 0 1 | 0+1=1
1 0 | 0 1 | 1+0=1
1 1 | 1 0 | 1+1=2
a | b | c | s
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 21: 4.7 Design of Binary Adders and Subtracters
Binary Adder for 4-bit Numbers
Binary adder composed of four full adders  Carry Ripple Adder

## Slide 22: 4.7 Design of Binary Adders and Subtracters
Truth Table for a Full Adder

## Slide 23: 4.7 Design of Binary Adders and Subtracters

## Slide 24
When 1’s complement is used, the end-around carry is accomplished by connecting C4 to C0 input.
Overflow(V) when adding two signed binary number
4.7 Design of Binary Adders and Subtracters

## Slide 25
Overflow(V) detection using hardware
4.7 Design of Binary Adders and Subtracters

## Slide 26
4.7 Design of Binary Adders and Subtracters
Binary Subtracter using full adder
Subtraction is done by adding the 2’s complemented number to be subtracted
2’s compleneted number : B’ + 1

## Slide 27
4.7 Design of Binary Adders and Subtracters
Full Subtracter
Full Subtracter
Full Subtracter
Full Subtracter
b n+1
d n
d i
d 2
d 1
x n
y n
x 3
y 3
x 2
y 2
x 1
y 1
b n
b i+1
b i
b 2
b 1=0
b 3
xi yi bi bi+1 di
0 0 0 0 0
0 0 1 1 1
0 1 0 1 1
0 1 1 1 0
0 0 0 1
1 0 1 0 0
1 0 0 0
1 1 1 1 1
Truth Table for a Full Subtracter