## Slide 1
Unit 15
This chapter in the book includes:
Objectives
Study Guide
15.1 Elimination of Redundant States
15.2 Equivalent States
15.3 Determination of State Equivalence Using an Implication Table
15.4 Equivalent Sequential Circuits
15.5 Incompletely Specified State Tables
15.6 Derivation of Flip-Flop Input Equations
15.7 Equivalent State Assignments
15.8 Guidelines for State Assignment
15.9 Using a One-Hot State Assignment
Problems
Reduction of State Tables and State Assignment

## Slide 2: Objectives
1. Define equivalent states, state several ways of testing for state equivalence, and determine if two states are equivalent.
2. Define equivalent sequential circuits and determine if two circuits are equivalent.
3. Reduce a state table to a minimum number of rows.
4. Specify a suitable set of state assignments for a state table, eliminating those assignments which are equivalent with respect to the cost of realizing the circuit.
5. State three guidelines which are useful in making state assignments, and apply these to making a good state assignment for a given state table.
6. Given a state table and assignment, form the transition table and derive flip-flop input equations.
7. Make a one-hot state assignment for a state graph and write the next state and output equations by inspection.

## Slide 3
A sequential circuit has one input (X) and one output (Z). The circuit examines groups of four consecutive inputs and produces an output Z = 1 if the input sequence 0101 or 1001 occurs. The circuit resets after every four inputs. Find a Mealy state graph. A typical input and output sequence is:
Example: Sequence Detector
15.1 Elimination of Redundant States

## Slide 4
Table 15-1: State Table for Sequence Detector
15.1 Elimination of Redundant States

## Slide 5
Since states H and I have the same next states and the same outputs, there is no way of telling states H and I apart.
We can replace I with H.
Table 15-2. State Table for Sequence Detector
15.1 Elimination of Redundant States

## Slide 6
Figure 15-1a: Reduced State Table for Sequence Detector
15.1 Elimination of Redundant States

## Slide 7
Figure 15-1b: Reduced State Graph for Sequence Detector
15.1 Elimination of Redundant States

## Slide 8
15.2 Equivalent States
Definition 15.1:
Let N1 and N2 be sequential circuits (not necessarily different). Let X represent a sequence of inputs of arbitrary length. Then state p in N1 is equivalent to state q in N2 iff 1(p, X) = 2(q, X) for every possible input sequence X.
Notes: 8

## Slide 9
Two states p and q of a sequential circuit are equivalent iff for every single input X, the outputs are the same and the next states are equivalent, that is,
where (p, X) is the output given the present state p and input X, and (p, X) is the next state given the present state p and input X. Note that the next states do not have to be equal, just equivalent.
15.2 Equivalent States
Theorem 15.1:

## Slide 10
a ≡ b iff
d ≡ f and c ≡ h
a ≡ d iff
a ≡ d and c ≡ e
15.3 Determination of Equivalent States
Table 15-3

## Slide 11
Figure 15-3: Implication Chart for Table 15-3
15.3 Determination of Equivalent States

## Slide 12
Figure 15-4: Implication Chart After First Pass
15.3 Determination of Equivalent States

## Slide 13
Figure 15-5: Implication Chart After Second Pass
15.3 Determination of Equivalent States

## Slide 14
d is replaced with a
e is replaced with c
d and e are removed
Table 15-4
15.3 Determination of Equivalent States

## Slide 15
The implication table method of determining state equivalence can be summarized as follows:
Implication Table Method:
Construct a chart which contains a square for each pair of states.
2. Compare each pair of rows in the state table. If the outputs associated with states i and j are different, place an X in square i-j to indicate that i ≡ j. If the outputs are the same, place the implied pairs in square i-j. (If the next states of i and j are m and n for some input x, then m-n is an implied pair.) If the outputs and next states are the same (or if i-j only implies itself), place a check (√) in square i-j to indicate that i ≡ j.
3. Go through the table square-by-square. If square i-j contains the implied pair m-n, and square m-n contains an X, then i ≡ j, and X should be placed in square i-j.
4. If any X’s were added in step 3, repeat step 3 until no more X’s are added.
5. For each square i-j which does not contain an X, i ≡ j.
15.3 Determination of Equivalent States

## Slide 16
15.4 Equivalent Sequential Circuits
Definition 15.2:
Sequential circuit N1 is equivalent to sequential circuit N2 if for each state p in N1, there is a state q in N2 such that p ≡ q, and conversely, for each state s in N2, there is a state t in N1 such that s ≡ t.
Notes: 16

## Slide 17
15.4 Equivalent Sequential Circuits
Figure 15-6: Graphs for Equivalent Circuits
Notes: 17

## Slide 18
15.4 Equivalent Sequential Circuits
Figure 15-7: Implication Tables for Determining Circuit Equivalence
Notes: 18

## Slide 19
15.5 Incompletely Specified State Tables
Figure 15-8
Assume that circuit A can only generate two possible output sequences, X = 100 and X = 110. Thus, the sequential circuit subsystem (B) has only two possible input sequences. Also, C only reads Z during everything third input.
Notes: 19

## Slide 20
15.5 Incompletely Specified State Tables
Table 15-5. Incompletely Specified State Table
Notes: 20

## Slide 21
15.6 Derivation of FF Input Equations
To derive the flip-flop input equations:
1. Assign flip-flop state values to correspond to the states in the reduced table.
2. Construct a transition table which gives the next states of the flip-flops as a function of the present states and inputs.
3. Derive the next-state maps from the transition table.
4. Find flip-flop input maps from the next-state maps using the techniques developed in Unit 12 and find the flip-flop input equations from the maps.
Notes: 21

## Slide 22
Assign flip-flop state values to correspond to the states in the reduced table.
Construct a transition table which gives the next states of the flip-flops as a function of the present states and inputs.
Example #1: Derivation of FF Input Equations (Table 15-6)
15.6 Derivation of FF Input Equations

## Slide 23
D FF Characteristic Equation:
Q+ = D
3. Derive the next-state maps from the transition table.
Example #1: Derivation of FF Input Equations (Figure 15-9 (a))
15.6 Derivation of FF Input Equations

## Slide 24
JK Excitation Table
Q | Q+ | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
4. Derive the flip-flop input maps from the next-state maps;
determine the flip-flop input equations from the FF input maps.
Example #1: Derivation of FF Input Equations (Figure 15-9 (b))
15.6 Derivation of FF Input Equations

## Slide 25
Assign flip-flop state values to correspond to the states in the reduced table.
Construct a transition table which gives the next states of the flip-flops as a function of the present states and inputs.
Example #2: Derivation of FF Input Equations (Table 15-7)
15.6 Derivation of FF Input Equations
Notes: 25

## Slide 26
D FF Characteristic Equation:
Q+ = D
3. Derive the next-state maps from the transition table.
Example #2: Derivation of FF Input Equations (Figure 15-10)
15.6 Derivation of FF Input Equations
Notes: 26

## Slide 27
4. Derive the flip-flop input maps from the next-state maps;
determine the flip-flop input equations from the FF input maps.
Example #2: Derivation of FF Input Equations (Figure 15-11)
15.6 Derivation of FF Input Equations
SR Excitation Table
Q | Q+ | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
Notes: 27

## Slide 28
Given a sequential circuit with three states and two flip-flops (A and
B), there are 4 × 3 × 2 = 24 possible state assignments for the three
states.
Table 15-8. State Assignments for 3-Row Tables
15.7 Equivalent State Assignments
Notes: 28

## Slide 29
When realizing a three-state sequential circuit with symmetrical flip-
flops (i.e. JK or SR), it is only necessary to try three different states
to be assured of a minimum cost realization.
Similarly, only three different assignments must be tried for four
states.
Table 15-10. Nonequivalent Assignments for 3 and 4 States
15.7 Equivalent State Assignments

## Slide 30
Table 15-11. Number of Distinct (Nonequivalent) State Assignments
15.7 Equivalent State Assignments

## Slide 31
Trying all nonequivalent state assignments is not practical in most cases. The following guidelines are useful in making assignments which will place 1’s (or 0's) together in the next-state maps:
1. States which have the same next state for a given input should be given adjacent assignments.
2. States which are the next states of the same state should be given adjacent assignments.
3. States which have the same output for a given input should be given adjacent assignments.
15.8 Guidelines for State Assignment
Notes: 31

## Slide 32
States which have the same next state for a given input should be given adjacent assignments.
States which are the next states of the same state should be given adjacent assignments.
States which have the same output for a given input should be given adjacent assignments.
Figure 15-16(a). State Table and Assignments
15.8 Guidelines for State Assignment

## Slide 33
Based on the State Assignment Guidelines:
1. (b, d) (c, f) (b, e)
2. (a, c) (d, f) (b, d) (b, f) (c, e)
3. (a, c) (b, d) (e, f)
Figure 15-16(b)(c). State Table and Assignments
15.8 Guidelines for State Assignment

## Slide 34
Table 15-12. Transition table for Figure 15-16(a)
15.8 Guidelines for State Assignment

## Slide 35
Figure 15-17. Next-State and Output Maps for Table 15-12
15.8 Guidelines for State Assignment

## Slide 36
15.9 Using a One-Hot State Assignment
Sometimes reducing the number of flip-flops used is not as important as reducing the logic feeding into the flip-flops. Using a one-hot state assignment may help accomplish this.
The one-hot assignment uses one flip-flop for each state, so a state machine with N states requires N flip-flops. Exactly one of the flip-flops is set to one in each state.

## Slide 37
State | Binary | Gray-code | One-hot
S0 | 00 | 00 | 0001
S1 | 01 | 01 | 0010
S2 | 10 | 11 | 0100
S3 | 11 | 10 | 1000
# of FF | 2 | 2 | 4
15.9 Using a One-Hot State Assignment
For a four-state FSM, three possible state assignments are:

## Slide 38: Logical SW Design: Final Recommendation
Integer 1~N Summation