## Slide 1
Unit 2 Boolean Algebra
This chapter in the book includes:
Objectives
Study Guide
2.1 Introduction
2.2 Basic Operation
2.3 Boolean Expression and Truth Table
2.4 Basic Theorem
2.5 Commutative, Associative, Distributive & DeMorgan’s Laws
2.6 Simplification Theorem
2.7 Multiplying Out and Factoring
2.8 Complementing Boolean Expressions

## Slide 2
Objectives
Topics introduced in this chapter:
  Understand the basic operations and laws of Boolean algebra
  Relate these operations & laws to AND, OR, NOT gates & switches
  Prove these laws using a truth table
  Manipulation of algebraic expression using
    Multiplying out
    Factoring
    Simplifying
    Finding the complement of an expression

## Slide 3
2.1 Introduction
Boolean algebra : Basic mathematics for logic design
Restrict to switching circuits
  Two state values: 0, 1
  Switching algebra
Boolean Variable
  X, Y, … can only have two state values (0, 1)
  Representing True(1), False(0)

## Slide 4
2.2 Basic Operations
NOT (Inverter)
Gate Symbol

## Slide 5
2.2 Basic Operations
A B | C = A · B
0 0 0 1 1 0 1 1 | 0 0 0 1
AND
Truth Table
Gate Symbol

## Slide 6
2.2 Basic Operations
A B | C = A + B
0 0 0 1 1 0 1 1 | 0 1 1 1
OR
Truth Table
Gate Symbol

## Slide 7
2.2 Basic Operations
Apply to Switch
AND
OR

## Slide 8
2.3 Boolean Expressions and Truth Tables
Logic Expression
Circuit of logic gates

## Slide 9
2.3 Boolean Expressions and Truth Tables
Logic Expression
Circuit of logic gates
Logic Evaluation : A=B=C=1, D=E=0
Literal : a variable or its complement in a logic expression
10 literals

## Slide 10: 2-Input Circuit and Truth Table
2.3 Boolean Expressions and Truth Tables
A B |  | A’ | F = A’ + B
0 0 0 1 1 0 1 1 |  | 1 1 0 0 | 1 1 0 1

## Slide 11
2.3 Boolean Expressions and Truth Tables
A B C |  |  | AB’ | AB’ + C |  | A + C | B’ + C | (A + C) (B’ + C)
0 0 0 0 0 1 0 1 0 0 1 1 1 0 0 1 0 1 1 1 0 1 1 1 |  | 1 1 0 0 1 1 0 0 | 0 0 0 0 1 1 0 0 | 0 1 0 1 1 1 0 1 |  | 0 1 0 1 1 1 1 1 | 1 1 0 1 1 1 0 1 | 0 1 0 1 1 1 0 1
TABLE 2.1
n times
n variable needs rows
Proof using Truth Table

## Slide 12: 2.4 Basic Theorems
Idempotent Laws
Involution Laws
Complementary Laws
Operations with 0, 1
Proof
Example

## Slide 13: 2.4 Basic Theorems
=
Circuit Examples
=
=
A
A

## Slide 14: 2.4 Basic Theorems
Circuit Examples
(A+1=1)
=
A’
(A+A’=1)
=
=
(A A’=0)