## Slide 1
Unit 1
This chapter in the book includes:
Objectives
Study Guide
1.1 Digital Systems and Switching Circuits
1.2 Number Systems and Conversion
1.3 Binary Arithmetic
1.4 Representation of Negative Numbers
1.5 Binary Codes
INTRODUCTION NUMBER SYSTEMS AND CONVERSION

## Slide 2
Chapter Objectives
Topics introduced in this chapter:
  Difference between Analog and Digital System
  Difference between Combinational and Sequential Circuits
  Binary number and digital systems
  Number systems and Conversion
  Add, Subtract, Multiply, Divide for Positive Binary Numbers
  1’s Complement, 2’s Complement for Negative binary number
  BCD code, 6-3-1-1 code, excess-3 code

## Slide 3: 1.1 Digital Systems and Switching Circuits
Digital systems are used extensively in computation, data processing, control, communication, and measurement
- Reliability, Integration, …
Analog – Continuous, uncountable
- Natural Phenomena
(Pressure, Temperature, Speed…)
- Difficulty in realizing, processing using electronics
Digital – Discrete, countable
- Binary Digit  Signal Processing as Bit unit
- Easy in realizing, processing using electronics
- High performance due to Integrated Circuit Technology

## Slide 4: Design of Digital Systems
System design
  Breaking the overall system into subsystems
  Specifying the characteristics of each subsystems
  System design of a digital computer system
    specifying the number and type of memory units, arithmetic units, and I/O devices
    Specifying the interconnection and control of these subsystems.
Three design levels: system design, logic design, circuit design
high-level low-level

## Slide 5: Design of Digital Systems
Logic design
  Determining how to interconnect basic logic blocks to perform a specific function
  An example is determining the interconnection of logic gates and flip-flops required to perform binary addition
Circuit design
  Specifying the interconnection of specific components such as resistors, diodes, and transistors to form a gate, flip-flops, or other logic blocks.
  Most contemporary circuit design is done in integrated form.
This book is largely devoted to a study of logic design!

## Slide 6: Switching Circuit
Combinational Circuit :
- outputs depend on only present inputs, not on past inputs
Sequential Circuit:
- outputs depend on both present inputs and past inputs
- have “memory” function

## Slide 7
Binary Digit?
Binary:- Two values(0, 1)
- Each digit is called as a “bit”
- Number representation with only two values (0,1)
- Can be implemented with simple electronics devices
(ex: Voltage High(1), Low(0)
Switch On (1) Off(0)…)
Good things in Binary Number

## Slide 8: 1.2 Number Systems and Conversion
Decimal
Binary
Radix (Base)
Octal
Hexadecimal

## Slide 9: 1.2 Number Systems and Conversion
Conversion of Decimal to Base-R

## Slide 10: 1.2 Number Systems and Conversion
53
2
26
2
13
2
6
2
3
2
1
2
rem. = 1 = a0
rem. = 0 = a1
rem. = 1 = a2
rem. = 0 = a3
rem. = 1 = a4
0
rem. = 1 = a5
Example: Decimal to Binary Conversion

## Slide 11: 1.2 Number Systems and Conversion
Conversion of a decimal fraction to Base-R
Example:

## Slide 12: 1.2 Number Systems and Conversion
Process starts repeating here because .4 was previously
obtained
Example: Convert 0.7 to binary

## Slide 13: 1.2 Number Systems and Conversion
45
7
6
7
0
rem.6
rem.3
Example: Convert 231.34 to base-7

## Slide 14: 1.2 Number Systems and Conversion
Example: Conversion of Binary to Octal or Hexa-decimal
(101011010111 )2 = ( )8, octal
(10111011)2 = ( ) 8, octal
(1010111100100101)2 = ( ) 16, hexadecimal
(1101101000)2 = ( ) 16, hexadecimal
1001101.010111 2 = 01001101.01011100 2 = 4D.5C 16

## Slide 15: 1.3 Binary Arithmetic
and carry 1 to the next column
carries
Addition
Example:

## Slide 16: 1.3 Binary Arithmetic
column 2
column 1
note borrow from column 1
note borrow from column 2
Subtraction Example with Decimal

## Slide 17: 1.3 Binary Arithmetic
and borrow 1 from the next column
(indicates
a borrow
From the
3rd column)
borrows
borrows
Subtraction
Example

## Slide 18: 1.3 Binary Arithmetic
multiplicand
multiplier
first partial product
second partial product
sum of first two partial products
third partial product
sum after adding third partial product
fourth partial product
final product (sum after adding fourth partial product)
Multiplication
Multiply: 13 x11(10)

## Slide 19: 1.3 Binary Arithmetic
The quotient is 1101 with a remainder of 10.
Division

## Slide 20: 1.4 Representation of Negative Numbers
Several representations of negative binary numbers are possible
  The sign and magnitude number system
  The 2’s complement number system (most popular)
  The 1’s complement number system

## Slide 21: 1.4 Representation of Negative Numbers
b
n
1
–
b
1
b
0
Magnitude
MSB
(a) Unsigned number
(b) Signed number
b
n
1
–
b
1
b
0
Magnitude
Sign
b
n
2
–
0 denotes +
1 denote -
MSB

## Slide 22: 1.4 Representation of Negative Numbers
2’s complement representation for Negative Numbers
Example:
1’s complement representation for Negative Numbers
Example:
2’s complement: 1’s complement + ‘1’

## Slide 23: 1.4 Representation of Negative Numbers
1111
1110
1101
1100
1011
1010
1001
1000
-
-
1111
1110
1101
1100
1011
1010
1001
1000
1000
1001
1010
1011
1100
1101
1110
1111
-
-0
-1
-2
-3
-4
-5
-6
-7
-8
0000
0001
0010
0011
0100
0101
0110
0111
+0
+1
+2
+3
+4
+5
+6
+7
1’s complement
2’s complement N*
Sign and
magnitude
Negative integers
-N
Positive
integers
(all systems)
+N
N

## Slide 24: 1.4 Representation of Negative Numbers
00000
00001
00010
11111
11110
10000
01111
10001
0
1
2
1
2
15
16
15
.
.
.
.
.
.
3
11101
4
11100
2’s complement representation for N = 5
Single zero

## Slide 25: 1.4 Representation of Negative Number
(correct answer)
wrong answer because of overflow
(+11 requires 5 bits including sign)
(correct answer)
Case 1
Case 2
Case 3
Addition of 2’s complement Numbers

## Slide 26: 1.4 Representation of Negative Numbers
correct answer when the last carry is ignored
(this is not an overflow)
wrong answer because of overflow
(-11 requires 5 bits including sign)
Case 5
Case 6
Addition of 2’s complement Numbers
correct answer when the carry from the sign bit
is ignored (this is not an overflow)
Case 4

## Slide 27: 1.4 Representation of Negative Numbers
(correct answer)
(end-around carry)
(correct answer, no overflow)
(end-around carry)
(correct answer, no overflow)
Case 3
Case 4
Case 5
Addition of 1’s complement Numbers

## Slide 28: 1.4 Representation of Negative Numbers
(end-around carry)
(wrong answer because of overflow)
Case 6
Addition of 1’s complement Numbers

## Slide 29: 1.4 Representation of Negative Numbers
(discard end-around carry)
Addition of 1’s complement Numbers
Addition of 2’s complement Numbers
(feed back end-around carry)
31
11100000
1
11011111
)
1
(
11101011
11110100
=

## Slide 30: 1.5 Binary Codes
Decimal Digit | 8-4-2-1 Code (BCD) | 6-3-1-1 Code | Excees-3 Code | 2-out-of-5 Code | Gray Code
0 1 2 3 4 5 6 7 8 9 | 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 | 0000 0001 0011 0100 0101 0111 1000 1001 1011 1100 | 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 | 00011 00101 00110 01001 01010 01100 10001 10010 10100 11000 | 0000 0001 0011 0010 0110 1110 1010 1011 1001 1000
Decimal | Gray code
0 | 0000
1 | 0001
2 | 0011
3 | 0010
4 | 0110
5 | 1110
6 | 1010
7 | 1011
8 | 1001
9 | 1000

## Slide 31: 1.5 Binary Codes
1010011 1110100 1100101 1110110 1100101
S t e v e
6-3-1-1 Code
ASCII (American Standard Code for Information Interchange)
refer Table 1-3
Try your Korean name. (i.e. 유재석)